CHELMSFORD, Mass. – (March 13, 2007) – Axis Communications, the global leader in the network video market, has introduced the first network dome camera with progressive scan capabilities to present moving objects without blur.  In addition to progressive scan, the AXIS 233D Network Dome Camera sets new standards by including a 35x optical zoom, wide dynamic range, and outstanding mechanical precision and speed.

The AXIS 233D is a day and night network dome camera designed for demanding security installations – such as airports, harbors, stadiums, casinos, and any location where it is necessary to view detailed video or follow distant objects.  It also includes professional features such as electronic image stabilizing, area zoom, image freezing between pre-set positions, and e-flip to automatically rotate video 180 degrees.

“The performance of the AXIS 233D far exceeds that of the best analog CCTV cameras, and there are no other network dome cameras on the market that can currently match its capabilities,” said Fredrik Nilsson, general manager for Axis Communications.  “The demand for dome cameras is increasing by 65 percent a year.  The AXIS 233D will ensure that Axis is well-positioned to capture a substantial share of that market growth.”

The AXIS 233D has the fastest pan/tilt performance of any dome camera on the market, with a maximum speed of 450 degrees a second between any of its 100 preset positions.  In addition, it offers precision movement of 0.05 degrees a second for slow tracking, making it possible to manually follow a walking person from approximately 1,300 feet.

The AXIS 233D delivers full frame rate video in all resolutions using MPEG-4 or Motion JPEG compression.

It also includes video motion detection, two-way audio, audio detection alarm, image upload, scheduled and triggered event functionality with alarm notification, four external input connections, and four relay outputs for controlling doors and lights.  It is protected through a comprehensive set of security features, including multiple user access levels, HTTPS encryption, IEEE 802.1X and IP address filtering.  The camera also supports Quality of Service (QoS) and Internet Protocol version 6 (IPv6) and IPv4 addresses.

The AXIS 233D is delivered with indoor mounting accessories, and a separate housing is available for outdoor use.  The product is supported by the industry’s largest base of application software through the Axis Application Development Partner program, as well as the AXIS Camera Station video management software.

The AXIS 233D is currently available through Axis’ distribution channels for the manufacturer’s suggested price of $2,499.

About Axis
Axis is an IT company offering network video solutions for professional installations. The company is the global market leader in network video, driving the ongoing shift from analog to digital video surveillance. Axis products and solutions focus on security surveillance and remote monitoring, and are based on innovative, open technology platforms.

Axis is a Sweden-based company, operating worldwide with offices in 18 countries and cooperating with partners in more than 70 countries. Founded in 1984, Axis is listed on the Nordic List, Mid Cap and Information Technology exchanges. For more information about Axis, please visit our website at www.axis.com.

Contact:

Sonia Taylor									Valerie Wehler

202-223-9260 ext. 223								978-614-2068

sonia@allisonpr.com								valerie.wehler@axis.com